## Slide 1: ClickOS and the Art of Network Function Virtualization
Joao Martins*, Mohamed Ahmed*, Costin Raiciu§, Roberto Bifulco*, Vladimir Olteanu§, Michio Honda*, Felipe Huici*
* NEC Labs Europe, Heidelberg, Germany
§ University Politehnica of Bucharest firstname.lastname@neclab.eu, firstname.lastname@cs.pub.ro

## Slide 2: The Idealized Network
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Transport
Application
Physical
Datalink
Network
Physical
Datalink

## Slide 3: A Middlebox World
carrier-grade NAT
load balancer
DPI
QoE monitor
ad insertion
BRAS
session border controller
transcoder
WAN accelerator
DDoS protection
firewall
IDS

## Slide 4: Hardware Middleboxes - Drawbacks
▐ Expensive equipment/power costs
▐ Difcult to add new features (vendor lock-in)
▐ Difcult to manage
▐ Cannot be scaled on demand (peak planning)

## Slide 5: Shifting Middlebox Processing to Software
▐ Can share the same hardware across multiple users/tenants
▐ Reduced equipment/power costs through consolidation
▐ Safe to try new features on a operational network/platform
▐ But can it be built using commodity hardware while still achieving high performance?
▐ ClickOS: tiny Xen-based virtual machine that runs Click

## Slide 6: From Thought to Reality - Requirements
ClickOS
30 msec boot times 5MB when running provided by Xen 10Gb/s line rate*
45 μsec delay
provided by Click
▐ Fast Instantiation
▐ Small footprint
▐ Isolation
▐ Performance
▐ Flexibility

## Slide 7: What's ClickOS ?
domU
apps
guest OS
paravirt
ClickOS
Click
mini OS
paravirt
▐ Work consisted of:
Build system to create ClickOS images (5 MB in size)
Emulating a Click control plane over MiniOS/Xen
Reducing boot times (roughly 30 milliseconds)
Optimizations to the data plane (10 Gb/s for almost all pkt sizes)
Implementation of a wide range of middleboxes

## Slide 8: Performance analysis
netback
packet size (bytes)
10 Gbit/s rate
64
14.88 Mp/s
128 8.4 Mp/s
256 4.5 Mp/s
512 2.3 Mp/s
1024 1.2 Mp/s
1500 810 Kp/s
Driver Domain (or Dom 0)
ClickOS Domain
Xen bus/store
Event channel
netfront
Xen ring API (data)
NW driver
OVS
300* Kp/s
350 Kp/s
225 Kp/s
* - maximum-sized packets
vif
Click
ToDevice
FromDevice

## Slide 9: Performance analysis
▐
Copying packets between guests greatly afects packet I/O (1)
▐
Packet metadata allocations (2)
▐
Backend switch is slow (3)
▐
MiniOS netfront not as good as Linux
netback
Driver Domain (or Dom 0)
ClickOS Domain
Xen bus/store
Event channel
netfront
Xen ring API
NW driver
OVS
vif
Click
ToDevice
FromDevice
772 ns (1)
~600 ns (2)
~3.4 us (3)

## Slide 10: Optimizing Network I/O – Backend Switch
netback
Driver Domain (or Dom 0)
ClickOS Domain
netfront
Xen bus/store | 
Event channel | 
Xen ring API
(data)
NW driver
(netmap mode)
port
Click
FromDevice
ToDevice
▐
Reuse Xen page permissions (frontend)
▐
Introduce VALE[1] as the backend switch
▐
Increase I/O requests batch size
VOAVLSE
[1] VALE, a switched ethernet for virtual machines, ACM CoNEXT'2012 Luigi Rizzo, Giuseppe Lettieri
Universita di Pisa

## Slide 11: Optimizing Network I/O
VALE
Driver Domain (or Dom 0)
ClickOS Domain
netfront
NW driver
Click
FromDevice
ToDevice
▐ Minimal memory requirements
–
For max. throughput a guest only needs 4 MB of memory
▐ Breaks other (non-MiniOS) guests
–
But we have implemented Linux netfront driver
slots | KB (per ring) | # grants (per ring)
64 | 135 | 33
128 | 266 | 65
256 | 528 | 130
512 | 1056 | 259
1024 | 2117 | 516
2048 | 4231 | 1033
netback netback
port
Xen bus/store
Event channel
NXentmrainpgAPI I (data)

## Slide 12: ClickOS Prototype Overview
▐ Click changes are minimal ~600 LoC
▐ New toolstack for fast boot times
▐ Cross compile toolchain for MiniOS-based apps
▐ netback changes comprise ~500 LoC
▐ netfront (Linux/MiniOS) around ~600 LoC
▐ VALE switch extended to:
– Connect NIC ports and modular switching

## Slide 13
EVALUATION

## Slide 14: Experiments
▐ ClickOS Instantiation
▐ State reading/insertion performance
▐ Delay compared with other systems
▐ Memory footprint
▐ Switch performance for 1+ NICs
▐ ClickOS/MiniOS performance
▐ Chaining experiments
▐ Scalability over multiple guests
▐ Scalability over multiple NICs
▐ Implementation and evaluation of middleboxes
▐ Linux Performance

## Slide 15: ClickOS Base Performance
Intel Xeon E1220 4-core 3.2GHz (Sandy bridge) 16GB RAM, 1x Intel x520 10Gb/s NIC.
One CPU core assigned to VMs, the rest to the Domain-0 Linux 3.6.10
ClickOS
Measurement Box
10Gb/s direct cable

## Slide 16: ClickOS Base TX Performance

## Slide 17: ClickOS (virtualized) Middlebox Performance
ClickOS
Host 2
Host 1
10Gb/s direct cable
10Gb/s direct cable
Intel Xeon E1220 4-core 3.2GHz (Sandy bridge) 16GB RAM, 2x Intel x520 10Gb/s NIC.
One CPU core assigned to Vms, 3 CPU cores Domain-0 Linux 3.6.10

## Slide 18: ClickOS (virtualized) Middlebox Performance

## Slide 19: Linux Guest Performance
▐ Note that our Linux optimizations apply only to netmap-based applications

## Slide 20: It's Open Source!
Checkout http://cnp.neclab.eu
ClickOS, Backend Switch, Xen optimizations and more!
Github ( https://github.com/cnplab )
Tutorials
Better performance!

## Slide 21: Conclusions
▐ Virtual machines can do fexible high speed networking
▐ ClickOS: Tailor-made operating system for network processing
Small is better: Low footprint is the key to heavy consolidation
Memory footprint: 5MB
Boot time: 30ms
▐ Future work:
Massive consolidation of VMs (thousands)
Improved Inter-VM communication for service chaining
Reactive VMs (e.g., per-fow)

## Slide 23: ClickOS Boot times
30 milliseconds
220 milliseconds

## Slide 24: Scaling out – Multiple NICs/VMs
Intel Xeon E1650 6-core 3.2GHz, 16GB RAM, dual-port Intel x520 10Gb/s NIC. 3 cores assigned to VMs, 3 cores for dom0
ClickOS
Host 2
6x 10Gb/s direct cable
6x 10Gb/s direct cable
Host 1

## Slide 25: Scaling out – 100 VMs Aggregate Throughput
Intel Xeon E1650 6-core 3.2GHz, 16GB RAM, dual-port Intel x520 10Gb/s NIC. 3 cores assigned to VMs, 3 cores for dom0

## Slide 26: ClickOS Delay vs. Other Systems